## Slide 1: Cache Memories 15-213: Introduction to Computer Systems 12th Lecture, Oct. 8, 2015
Instructors:
Randal E. Bryant and David R. O’Hallaron

## Slide 2: Today
Cache memory organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 3: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 4: General Cache Concept
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 5: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware
  Hold frequently accessed blocks of main memory
CPU looks first for data in cache
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memory

## Slide 6: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 7: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 8: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 9: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag

## Slide 10: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
If tag doesn’t match: old line is evicted and replaced

## Slide 11: Direct-Mapped Cache Simulation
M=16 bytes (4-bit addresses), B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3

## Slide 12: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 13: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 14: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 15: 2-Way Set Associative Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 16: What about writes?
Multiple copies of data exist:
  L1, L2, L3, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes straight to memory, does not load into cache)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 17: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.

## Slide 18: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    4 clock cycle for L1
    10 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 19: Let’s think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 20: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories

## Slide 21: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 22: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 23: Memory Mountain Test Function
long data[MAXELEMS]; /* Global array to traverse */
/* test - Iterate over first "elems" elements of
* array “data” with stride of "stride", using
* using 4x4 loop unrolling.
*/
int test(int elems, int stride) {
long i, sx2=stride*2, sx3=stride*3, sx4=stride*4;
long acc0 = 0, acc1 = 0, acc2 = 0, acc3 = 0;
long length = elems, limit = length - sx4;
/* Combine 4 elements at a time */
for (i = 0; i < limit; i += sx4) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+stride];
acc2 = acc2 + data[i+sx2];
acc3 = acc3 + data[i+sx3];
}
/* Finish any remaining elements */
for (; i < length; i++) {
acc0 = acc0 + data[i];
}
return ((acc0 + acc1) + (acc2 + acc3));
}
Call test() with many combinations of elems
and stride.
For each elems and stride:
1. Call test() once to warm up the caches.
2. Call test() again and measure the read throughput(MB/s)
mountain/mountain.c

## Slide 24: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching

## Slide 25: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 26: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  Matrix elements are doubles (8 bytes)
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register
matmult/mm.c

## Slide 27: Miss Rate Analysis for Matrix Multiply
Assume:
  Block size = 32B (big enough for four doubles)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j
=
x

## Slide 28: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > sizeof(aij) bytes, exploit spatial locality
    miss rate = sizeof(aij) / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    miss rate = 1 (i.e. 100%)

## Slide 29: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0
matmult/mm.c

## Slide 30: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0
matmult/mm.c

## Slide 31: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
matmult/mm.c

## Slide 32: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
matmult/mm.c

## Slide 33: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c

## Slide 34: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c

## Slide 35: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 36: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700
jki | 4.8 | 4.68 | 4.65 | 4.8 | 6.84 | 15.03 | 22.78 | 29.39 | 40.39 | 57.06 | 60.54 | 63.33 | 65.61 | 67.49
kji | 4.83 | 4.72 | 4.64 | 4.69 | 6.83 | 15.1 | 22.68 | 29.18 | 40.26 | 57.02 | 60.53 | 63.34 | 65.62 | 67.53
ijk | 3.75 | 4.08 | 4.33 | 4.45 | 4.45 | 4.45 | 4.45 | 4.47 | 7.73 | 18.77 | 20.36 | 21.67 | 22.76 | 23.71
jik | 3.93 | 4.14 | 4.36 | 4.47 | 4.52 | 4.56 | 4.57 | 4.6 | 7.96 | 19.05 | 20.59 | 21.86 | 22.92 | 23.82
kij | 1.86 | 1.78 | 2.14 | 2.3 | 2.23 | 2.18 | 2.14 | 2.12 | 2.12 | 2.13 | 2.13 | 2.14 | 2.16 | 2.22
ikj | 1.78 | 1.8 | 2.12 | 2.03 | 1.96 | 1.92 | 1.89 | 1.86 | 1.86 | 1.88 | 1.89 | 1.9 | 1.91 | 1.95
ijk / jik
jki / kji
kij / ikj

## Slide 37: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 38: Example: Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n + j] += a[i*n + k] * b[k*n + j];
}

## Slide 39: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide

## Slide 40: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3
n
*
=
8 wide

## Slide 41: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=B)
for (j = 0; j < n; j+=B)
for (k = 0; k < n; k+=B)
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i1++)
for (j1 = j; j1 < j+B; j1++)
for (k1 = k; k1 < k+B; k1++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
c
+
Block size B x B
matmult/bmm.c

## Slide 42: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
First (block) iteration:
  B2/8 misses for each block
  2n/B * B2/8 = nB/4 (omitting matrix c)
  Afterwards in cache (schematic)
*
=
*
=
Block size B x B
n/B blocks

## Slide 43: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Second (block) iteration:
  Same as first iteration
  2n/B * B2/8 = nB/4
Total misses:
  nB/4 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 44: Blocking Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
Suggest largest possible block size B, but limit 3B2 < C!
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly

## Slide 45: Cache Summary
Cache memories can have significant performance impact
You can write your programs to exploit this!
  Focus on the inner loops, where bulk of computations and memory accesses occur.
  Try to maximize spatial locality by reading data objects with sequentially with stride 1.
  Try to maximize temporal locality by using a data object as often as possible once it’s read from memory.